## Slide 1: Sampling Rotation Groups using Halton Sequence and Hopf Coordinates
Wai-Shing Luk
luk@fudan.edu.cn
(confidential)

## Slide 2: Abstract
Sampling SO(3) rotation groups has a wide range of applications, such as
  Robotic Motion Planning
  Computational Chemistry and Biology
  Computer Graphic
We propose a simple yet effective method which:
  Utilizes low-discrepancy sequence, and
  Hopf coordinates for SO(3)
  Contains only 10 lines of MATLAB code in our implementation!
  Allow incremental generation.
Numerical results shows that the proposed method outperforms the randomly generated sequences …

## Slide 3: Overview
Motivation and applications
Review of Low discrepancy sequence
  Van der Corput sequence on [0,1]
  Halton sequence on [0,1]d
  Halton sequence on sphere (i.e. S2)
S3 and SO(3) using Hopf coordinate
Numerical Experiments
Conclusion

## Slide 4: Introduction

## Slide 5: Sampling SO(3) Occurs in:
Motion Planning (generate good paths in C-space)
Automotive Assembly
Computational Chemistry and Biology
Manipulation Planning
Medical applications
Computer Graphics (motions for digital actors)
Autonomous vehicles and spacecrafts
Notes: Rotation

## Slide 6: Problem Formulation
Desirable properties of samples over the SO(3):
  Uniform and Incremental
    The uniformity measures are optimized with every new point.
    Reason: it is unknown how many points are needed to solve the problem in advance

## Slide 7: Halton Sequence & Hopf Coordinates
On one hand, Halton sequence on S2 has been well studied for S2 [CuiFreeden 97, WongLuk97] by using cylindrical mapping.
Yet it is still unknown for S3 and SO(3)
On the other hand, Hopf coordinates are used for generating uniform grid points on S3 and SO(3) [Yershova et. al. 2010].
In this talk, we combine this two techniques.

## Slide 8: Review of Halton sequence

## Slide 9: Basic: Van der Corput sequence
Generate low discrepancy sequence over [0, 1]
Denote vd(k,b) as a Van der Corput sequence of k points, where b is the base number.
Matlab code is available at http://www.mathworks.com/matlabcentral/fileexchange/15354-generate-a-van-der-corput-sequence

## Slide 10: Unit Square [0,1] x [0,1]
Halton sequence: using 2 Van der Corput sequences with coprime bases. For example:
  [x, y] = [vd(k,2), vd(k,3)]

## Slide 11: Unit Hypercube [0, 1]d
Generally we can generate Halton sequence in a unit hypercube [0, 1]d
  [x1, x2, x3, …, xd] = [vd(k,b1), vd(k,b2), … vd(k,bd)]
A wide range of applications on Quasi-Monte Carlo Methods (QMC).
  Low discrepancy
  Incremental generation

## Slide 12: Unit Circle S1
Can be generated by mapping the Van der Corput sequence to [0, 2π]:
   = 2π * vd(k, b)
  [x, y] = [cos(), sin()]
Generalized discrepancy can be defined. Work very well on both straight lines and circles.

## Slide 13: Unit Sphere S2
  Cylindrical mapping is used:
  [x, y, z] = [(1-z2) cos(), (1-z2) sin(), z]
 = 2π * vd(k, b1) % map to [0, 2π]
z = 2*vd(k, b2) – 1 % map to [-1, 1]
Has been applied for computer graphic applications [WongLuk 97]

## Slide 14: Spheres S3 and SO(3)
Random sequences:
  To generate random points on Sd, spherical symmetry of the multidimensional Gaussian density function can be exploited.
  Then the normalized vector (xi/||xi||) is uniformly distributed over the hypersphere Sd.
  [Fishman, G. F. (1996)]
Deterministic point sets
  Optimal discrepancy point sets for Sd, SO(3)
  [Lubotzky, Phillips, Sarnak 86] [Mitchell 07]
No Halton sequences to our knowledge
Notes:   To generate uniformly distributed random points on a hypersphere Sd, spherical symmetry of the multidimensional Gaussian density function can be exploited (Fishman 1996). Then the normalized vector (xi/||xi||) is uniformly distributed over the hypersphere S^d.
Fishman, G. F. (1996). Monte Carlo: Concepts, Algorithms, and Applications. Berlin, Springer.
Mitchell, J. C. (2007). Sampling rotation groups by successive orthogonal images. SIAM Journal on Scientific Computing, 30(1): 525–547.

## Slide 15: Hopf coordinates

## Slide 16: SO(3) Coordinates
Spherical coordinates:
  x1 = cos(3)
  x2 = sin(3) cos(2)
  x3 = sin(3) sin(2) cos(1)
  x4 = sin(3) sin(2) sin(1)
Hopf coordinate (cf. Yershova et. al. 2010):
  x1 = cos(/2) cos(/2)
  x2 = cos(/2) sin(/2)
  x3 = sin(/2) cos( + /2)
  x4 = sin(/2) sin( + /2)

## Slide 17: How is it related the rotations?
???

## Slide 18: Hopf Coordinates for SO(3) or S3
Similar to the Halton seqeuce generation on S2, we perform the mapping:
   = 2π * vd(k, b1) % map to [0, 2π]
   = 2π * vd(k, b2) % map to [0, 2π] for SO(3),
  or  = 4π * vd(k, b2) % map to [0, 4π] for S3
  z = 2*vd(k, b3) – 1 % map to [-1, 1]
   = cos-1z

## Slide 19: 10 Lines of MATLAB code for S3
function[s] = sphere3_hopf(k,b)
% sphere3_hopf Halton sequence
phi = 2*pi*vdcorput(k,b(1)); % map to [0, 2*pi]
psy = 4*pi*vdcorput(k,b(2)); % map to [0, 4*pi]
z = 2*vdcorput(k,b(3)) - 1; % map to [-1, 1]
theta = acos(z);
cos_eta = cos(theta/2);
sin_eta = sin(theta/2);
s = [cos_eta .* cos(psy/2), ...
cos_eta .* sin(psy/2), ...
sin_eta .* cos(phi + psy/2), ...
sin_eta .* sin(phi + psy/2)];

## Slide 20: Numerical experiment

## Slide 21: Testing the Correctness
Compare the discrepancy with the random point-set.
  Construct the convex hull for each point-set.
  Discrepancy roughly measured by the determinant of the largest facet:
    max |det([1, p1– p0, p2– p0, … pn– p0,])|
Better idea???
Notes: To generate uniformly distributed random points on a hypersphere Sd, spherical symmetry of the multidimensional Gaussian density function can be exploited (Fishman 1996). Then the normalized vector (xi/||xi||) is uniformly distributed over the hypersphere S^d.
Fishman, G. F. (1996). Monte Carlo: Concepts, Algorithms,
and Applications. Berlin, Springer.

## Slide 22: Convex Hull with ~400 points on S2
Low discrepancy point-set
Randomly generated point-set

## Slide 23: Dispersion. (S2, red – our, blue – Rand)

## Slide 24: Disperson. (S3, blue – our, red – Rand)

## Slide 25: Conclusions
Proposed a simple yet effective method that generates low-discrepancy point set in nearly linear time.
The result outperforms the corresponding randomly generated point set, especially when the number of points is small.

## Slide 26: Any Suggestions?