## Slide 1: PDK Abstraction for ALIGN

## Slide 2: PDK Abstraction
We abstract BEOL/MEOL and FEOL layers design rules for a PDK
  Each BEOL/MEOL and FEOL layer has a set of abstracted design rules
We store these rules in a JSON format file
  This file is used across different modules in ALIGN tool
Advantages of PDK abstraction
  Portable across processes
  Abstracted PDK links to other tools
  Simplifies design rules, enables improved code quality
This presentation summarizes steps to create JSON file (abstracted rules) for a given PDK

## Slide 3: PDK Abstraction: ‘layers.json’
Defines abstracted design rules for BEOL/MEOL/FEOL in a pdk
We store these rules in a JSON format file
This file is used across different modules in ALIGN tool

## Slide 4: PDK Abstraction: ‘layers.json’
Defines abstracted design rules for BEOL/MEOL/FEOL in a pdk
We store these rules in a JSON format file
This file is used across different modules in ALIGN tool
Pitch
End-to-End

## Slide 5: PDK Abstraction: ‘models.sp’
Define models for devices available in a pdk
The model names are used in ‘annotation phase’
  To recognize devices in a netlist
.modelsky130_fd_pr__pfet_01v8 pmos w=1 l=1
.model sky130_fd_pr__nfet_01v8 nmos w=1 l=1

## Slide 6: PDK Abstraction: ‘mos/cap/res.py’
Generators for MOS/CAP/RES devices
Minor modification may be required based on a pdk
MOS
Poly RES
MIM Cap

## Slide 7: PDK Abstraction: Assumptions
We will explain the abstraction considering a pdk
  With N metal layers (including MEOL)
  With N-1 vias
Metal names in the ‘layers.json’ must start with ‘M’
  For example, M1, M2, …., MN
Via names in the ‘layers.json’ must start with ‘V’
  For example, V1, V2, ….., VN-1
Do not use FEOL layer names starting with ‘M’ or ‘V’
All dimensions are in nanometer

## Slide 8: Design Rule Abstraction: Vias
Step1: Decide the number of vias V1, V2, … VN-1 (except V0)
  Maximum V0 are placed automatically based on active width
We use two type of vias in ALIGN
  Single via (Fig. 1) and Via array (Fig. 2)
    NumX and NumY define the number of vias in X- and Y- direction, respectively
Via
Metal
NumX:3
NumY:2
NumX:2
NumY:2
Fig. 1
Fig. 2

## Slide 9: Design Rule Abstraction: Single Via
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
  “Stack”: Metal layers which are connected using the Via
  “SpaceX”/”SpaceY”: Minimum spacing between two vias in X/Y direction (Fig. 1)
  “WidthX/WidthY”: Via widths in X/Y direction
  “VencA_L/VencA_H(VencP_L/VencP_H)”: Minimum enclosure of a Via by a lower/higher metal layer along its ‘Direction’ (Perpendicular to its ‘Direction’) as shown in Fig. 2
  “R”: Resistance per via (not required to run the tool, you can leave it as)
Via
Metal
SpaceY
SpaceX
Fig. 1
Fig. 2

## Slide 10: Design Rule Abstraction: Via array
Definition of parameters:
  “Layer”, “GdsLayerNo”, “GdsDatatype”, “Stack”, definition is same as for a single via
  “SpaceX”/”SpaceY”: Minimum spacing between two vias in X/Y direction
  “VencA_L/VencA_H(VencP_L/VencP_H)”: Minimum enclosure of a Via by a lower/higher metal
  layer along its ‘Direction’ (Perpendicular to its ‘Direction’; same as for a single via)
  “ViaCut” parameters:
    “Gen”: This define the name of via array generator. Use “ViaArrayGenerator” for it.
    “WidthX/WidthY”: This defines single Via widths in X/Y direction
    ***“SpaceX”/”SpaceY”: Minimum spacing between two vias in X/Y direction
    “NumX”/”NumY”: Number of vias in X/Y direction (Fig. 1)
  “WidthX” = NumX*(WidthX of ViaCut) + (NumX-1)*(SpaceX of ViaCut)
  “WidthY” = NumY*(WidthY of ViaCut) + (NumY-1)*(SpaceY of ViaCut)
Fig. 1
NumX:3
NumY:2
NumX:2
NumY:2
***“SpaceX”/”SpaceY” are same in “ViaCut” and outside of it

## Slide 11: Design Rule Abstraction: Metal/Poly
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
  “Direction”: Defines the allowed direction for the layer e.g., V (Vertical) or H (Horizontal)
  “Color”: Define available coloring patterns for the layer e.g., [C1, C2] or [] (Leave it blank if only single color allowed)
  “Pitch”: Center-to-Center distance for a layer (Shown in next slide Fig. 1)
  “Width”: Define width of the layer
  “MinL”: Minimum length of a layer; Please note that the length is along a layer ‘Direction’
  “MaxL”: Maximum allowed length for a layer (null means infinite; If there is no max limit in the PDK keep it null)
  “EndToEnd”: Minimum end-to-end spacing for a layer (Shown on next slide Fig. 2)
  “Offset”: Defines a layer offset from X or Y- axis; It is shown for a layer in V direction (Shown on next slide Fig. 3)
  “UnitC”: Per micrometer length capacitance for a layer
  “UnitCC”: Per micrometer length coupling capacitance for a layer
  “R”: Per micrometer length resistance for a layer

## Slide 12: Design Rule Abstraction: Metal/Poly
Pitch
End-to-End
Fig. 2
Fig. 1
Fig. 3
Offset
End-to-End
Fig. 2
Offset
These are some checks and might help in PDK abstraction:
Exact values of “UnitC”, “UnitCC”, and “R” are not required to run the tool, you can leave them as it is
“MinL” rule can be found out in the PDK using Min Area rule: Min Area = “MinL” * “Width”
Keep “Offset” = 0 for all metal layers; for “Poly” layer “Offset” = “Pitch”/2
“M1” and “Poly” “Pitch” must be same to generate a correct layout
“M3” “Pitch” must be multiple of “M1” “Pitch” for the correct functionality of the tool
If you have a FinFET PDK “M2” “Pitch” is constrained by “Fin” “Pitch” (see the next slide)
To find out poly pitch draw a two-finger transistor using pcells in your pdk and calculate center to center distance
Y-axis, X = 0

## Slide 13: Design Rule Abstraction: Fin
Parameters definition is same as for Metal/Poly layers
“Direction” is always “H” for “Fin” layer
“Offset” is 0 for “Fin” layer
For a bulk PDK:
  Use “Pitch” = half of M2 “Pitch” and leave other parameters as it is
  We will remove the “Fin” layer for bulk PDKs In future releases
For FinFET PDKs:
  Make sure that M2 “Pitch” = 2* Fin “Pitch” (Contact us if you want to use a different value)

## Slide 14: Design Rule Abstraction: FEOL -> Nwell/Nselect/Pselect
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
In your PDK Nselect/Pselect can be with names like N+/P+ or NN/PP

## Slide 15: Design Rule Abstraction: FEOL -> RVT/LVT/HVT/SLVT
These layers define VT (threshold voltage) type for a device
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
In your PDK you may have SVT (standard VT) or ELVT (extreme low VT), etc.

## Slide 16: Design Rule Abstraction: FEOL -> Active
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
  “active_enclosure”: Defines enclosure of “Active” layer by VT layer (RVT, LVT, etc.) as shown in Fig. 1
  “activebWidth”: “Active” width for body contact
  “activebWidth_H”: “Active” width in horizontal direction
  “activePolyExTracks”: It defines the distance between “Active” and poly contact
  in terms of number of M2 tracks (Shown in Fig. 2) e.g., 2 will result in 2*M2.”Picth”
  distance between active and poly contact
Active
active_enclosure
active_enclosure
VT layer
Fig. 1
Active
Poly contact
“activePolyExTracks”
Fig. 2
= 2*V0.”Width”

## Slide 17: Design Rule Abstraction: FEOL -> Pc
“Pc” is poly connect layer
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
  “PcWidth”: Defines the width (Shown in Fig. 1)
  “PcExt”: “Pc” extension over poly layer
For Bulk PDKs:
  Poly is used as a contact layer
  Use poly layer “GdsLayerNo” for “Pc” layer (do not delete it)
  “PcWidth” = 2*(”Width” of V0 layer)
  “PcExt” = 0
Active
Poly contact
Fig. 1
PcWidth
PcExt

## Slide 18: Design Rule Abstraction: FEOL -> Pb
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation
  “pbWidth”: “Pb” width for body contact
  “pbWidth_H”: “Pb” width in horizontal direction
“Pb” is used in body contact only
  In some pdks an extra layer other than
  active/Nselecet/Pselect/Nwell is used
  If in your pdk this layer is not used leave “Pb”
  layer as it is in layers.json (do not delete)
Active
pb_Width
Pb layer
Fig. 1
pb_Width_H

## Slide 19: Design Rule Abstraction: Boundary Layers -> Bbox/Boundary/Outline/R/C-boundary
These layers defines boundary/outline around the layout
  If not required in your pdk leave them as it is.
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation

## Slide 20: Design Rule Abstraction: MOM Cap
ALIGN has in built MOM cap cells
  It uses M1, M2 and M3 metal layers
Caps layouts are very specific to a PDK, therefore, we do not have a generalized template
Definition of parameters:
  “Layer”: Defines a layer name
  “GdsLayerNo”: Used for layer mapping in GDSII generation
  “GdsDatatype”: Layer data type used in GDSII generation

## Slide 21: How to Generate a Primitive
Run the following commands in your installed ALIGN pdk directory
The following commands will generate a differential pair GDSII
  - b : defines block name, you can use any name for it. In this example ‘test’ is used
Import the generated GDS in Cadence virtuoso and run DRC checks for your PDK
  If there are any DRCs please contact us.